## Slide 1
ST2 GPU: An Energy-Efficient GPU Design with
Spatio-Temporal Shared-Thread Speculative Adders
Vijay Kandiah, Ali Murat Gok, Georgios Tziantzioulis, Nikos Hardavellas
Notes: Hello everyone, I am Vijay Kandiah from Northwestern University and today I’m going to talk to you about ST2 GPU.

## Slide 2: GPUs are Important Systems
Widespread adoption of GPUs (AI, machine learning, HPC, ...)
  70% of top 50 HPC applications are GPU-accelerated
  29% of TOP500 supercomputer systems are GPU-accelerated (and growing)
% TOP500 systems with GPUs
Chart: 
| NVIDIA Volta GV100 | NVIDIA Pascal GP100 | NVIDIA Ampere GA100 | NVIDIA Tesla K40 | NVIDIA Tesla K80 | AMD Vega 20 | NVIDIA Tesla K20x | NVIDIA 2050 | NVIDIA Tesla K40m | NVIDIA Tesla K40 | NVIDIA Tesla P100 NVLink | Nvidia Volta V100 | NVIDIA Tesla K20m
 | 0.218 | 0.026 | 0.012 | 0.006 | 0.004 | 0.002 | 0.002 | 0.002 | 0.002 | 0.002 | 0.002 | 0.002 | 0.002
% TOP500 systems with GPUs
Notes: Now, GPUs have become important architectures in various domains like Artificial Intelligence, Machine Learning , and High-Performance Computing.
For instance, 29% of systems in the most recent TOP500 list are now GPU-accelerated.

## Slide 3: Core Count Increases but Power Stays Same
Chart: CUDA Cores
| Fermi GF100 (2010) | Fermi GF110 (2011) | Kepler GK104 (2012) | Kepler GK110 (2013) | Maxwell GM200 (2015) | Pascal GP100 (2016) | Pascal GP102 (2017) | Volta GV100 (2017) | Turing TU102 (2018) | Ampere GA100 (2020) | Ampere GA102 (2020)
CUDA Cores | 480 | 512 | 1536 | 2880 | 3072 | 3584 | 3840 | 5120 | 4608 | 6912 | 10752
TDP | 250 | 244 | 195 | 230 | 250 | 235 | 250 | 250 | 250 | 250 | 300
Fewer Watts per CUDA core
Notes: Designers continue to cram increasingly more cores per GPU chip to meet ever-increasing performance targets. This leads to a commensurate rise in power consumption.
However, the power budget of modern GPUs is already at the limit of practical cooling technology with a Thermal Design Power of around 250 Watts.
In order to continue increasing the number of cores within a GPU at a constant power budget, these cores must become more energy efficient.

## Slide 4: GPU Workloads Perform a lot of Additions
>20% of executed instrs. are ALU & FPU instrs. in 21 of 23 kernels
Chart: Dynamic Instructions
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Average
ALU Add | 0.090694 | 0.29878 | 0.13217 | 0.2449 | 0.15168 | 0.14815 | 0.19127 | 0.12971 | 0.41675 | 0.27955 | 0.17073 | 0.20924 | 0.30153 | 0.4389 | 0.32319 | 0.39597 | 0.33127 | 0.50098 | 0.36684 | 0.47987 | 0.21762 | 0.5127 | 0.058283 | 0.27786
ALU Other | 0.00017113 | 0.042768 | 0.0063227 | 0.26531 | 0.061075 | 0.16667 | 0.13915 | 0.14644 | 0.23609 | 0.243 | 0.069071 | 0.17926 | 0.18752 | 0.25486 | 0.21366 | 0.26963 | 0.23529 | 0.26927 | 0.34683 | 0.32856 | 0.57948 | 0.28597 | 0.8878 | 0.2354
FPU Add | 0.00068417 | 0.14558 | 0 | 0.16327 | 0 | 0.018519 | 0.10431 | 0.159 | 0 | 0 | 0.068008 | 0.059338 | 0 | 0 | 0 | 0 | 0.13622 | 0 | 0 | 0 | 0 | 0 | 0 | 0.037171
FPU Other | 0.000684 | 0.01331 | 0.00077224 | 0 | 0 | 0.16667 | 0.078231 | 0 | 0 | 0 | 0.10745 | 0.069956 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.041483 | 0.014481 | 0 | 0.0096386 | 0.021855
Other | 0.90777 | 0.49956 | 0.86073 | 0.32653 | 0.78724 | 0.5 | 0.48704 | 0.56485 | 0.34716 | 0.47745 | 0.58474 | 0.4822 | 0.51095 | 0.30624 | 0.46315 | 0.3344 | 0.29721 | 0.22976 | 0.28633 | 0.15008 | 0.18842 | 0.20133 | 0.044277 | 0.42771
32% ALU+FPU Adds
Notes: Often, ALUs and FPUs are exercised intensely by workloads: 21 out of 23 kernels from popular GPU benchmark suites exhibit high arithmetic intensity.

## Slide 5: Motivation
Widespread adoption of GPUs (AI, machine learning, HPC, ...)
Fewer Watts per CUDA core
High arithmetic intensity in GPU workloads
We need low power adders in GPUs!
Notes: Thus, to make the cores more energy efficient, low power adders are needed, and we propose a solution in this work.

## Slide 6
Conventional adder:
Clock period
64-bit KSA
Voltage-Scaled Sliced Adders
Notes: To make adders that consume less power, let’s start with a traditional 64-bit Kogge-Stone adder with a reference clock period indicated here.

## Slide 7
Conventional adder:
Sliced adder:
Clock period
64-bit KSA
8-bit KSA
Slice 0
8-bit KSA
Slice 1
8-bit KSA
Slice 2
Carry
Carry
Carry
Clock period
...
Voltage-Scaled Sliced Adders
Notes: It’s possible to create an adder with the same functionality by using smaller sized adders, but in this case each adder should wait for the lower sub-adder to finish and get the correct carry from it.
Thanks to super-linear hardware scaling, total area is reduced in this design; but these sub-adders should run one after another in a serial way, causing total delay to be larger.

## Slide 8
Conventional adder:
Sliced speculative adder:
Clock period
64-bit KSA
...
Speculated
Carry
Carry Prediction
...
Speculated
Carry
Clock period
8-bit KSA
8-bit KSA
8-bit KSA
Slice 0
Slice 1
Slice 2
Time slack
Voltage-Scaled Sliced Adders
Notes: If we break the carry propagation chain and provide a speculated carry to each sub-adder, we can run all of them in parallel.
The resulting design is a “Sliced Speculative Adder”.
Typically, Sliced Speculative Adders have smaller delay than the reference circuit.

## Slide 9
Conventional adder:
Voltage-scaled sliced adder:
Clock period
64-bit KSA
...
Speculated
Carry
Carry Prediction
...
Speculated
Carry
Clock period
Slice 0
Slice 1
Slice 2
Voltage-Scaled Sliced Adders
8-bit Vdd-scaled KSA
8-bit Vdd-scaled KSA
8-bit Vdd-scaled KSA
Notes: The remaining timing budget can be exchanged for lower power consumption by decreasing the supply voltage.
So, we can decrease the supply voltage, causing the slices to be linearly slower, until they utilize all of the available timing budget.
Thus, performance is not affected, but we decrease power consumption quadratically.

## Slide 10
Conventional adder:
Voltage-scaled sliced adder:
Clock period
64-bit KSA
...
Speculated
Carry
Carry Prediction
...
Speculated
Carry
Clock period
8-bit Vdd-scaled KSA
8-bit Vdd-scaled KSA
8-bit Vdd-scaled KSA
Slice 0
Slice 1
Slice 2
We need innovation in:
Accurate and efficient carry prediction
Guaranteed correctness
Integration into GPU pipeline
Voltage-Scaled Sliced Adders
Notes: To achieve this, we need accurate and efficient carry prediction.
This can be done with additional circuitry in each slice that coordinates with a new carry speculation unit.
We also need to integrate this speculation unit and the adders into the GPU pipeline.
Additionally, we need to have a fallback mechanism to guarantee correctness in the event of carry mispredictions.

## Slide 11: Carry Prediction in GPUs is Challenging
Must be accurate
  Correctness required, but 2x latency to fix each misprediction
  One thread mispredicts  all 32 threads in warp stalled for 2x cycles
Must be efficient
  GV100: 815 mm2 @ 1.45GHz  need fast predictions with practically no area overhead
  5,120 ALU & 5,120 FPU cores  >66,000 predictions per cycle, per chip
Must be integrated into GPU pipeline
  163,840 concurrent threads  Too much bookkeeping & contention on history updates
  Variable latency ADDs to guarantee correctness
Notes: Why is carry prediction challenging in GPUs?
First, predictions must be accurate. Correctness is a requirement, but we need twice the cycles to recover from mispredictions and guarantee correctness.
Threads in GPUs execute in bunches of 32, called warps.
Thus, to make it worse, when a thread mispredicts, all 32 threads in the warp are stalled for twice the cycles.\
Second, predictions must be efficient. A GV100 chip is already 815mm2, so we cannot afford too much area overhead,
It runs at 1.45GHz, so predictions must also be fast. Yet, GV100 has 5120 CUDA cores. We need to predict 7 carry-ins for each ALU, which amounts to >35,000 predictions per cycle, per chip.
Actually, it is almost twice that, because we predict for FPU ADDs as well, and FPUs can run concurrently with ALUs, so we need to support >66,000 predictions per cycle, per chip, at 1.45GHz, with practically no area overhead. \
If we now consider that a GPU chip runs almost 165,000 threads concurrently, there is simply too much bookkeeping taking place and possibly too much contention on history reads and updates.
Additions are also variable-latency now, as we need to guarantee correctness.
So, we must integrate our design into the GPU pipeline in a way that supports almost-always-correct predictions, at a rate of >66,000 predictions every 700 ps, with practically no area overhead, and without disrupting the rest of the pipeline despite the inordinate amount of concurrency in GPUs.
This is hard !!!

## Slide 12
Observe & quantify spatio-temporal value correlation
Design-space exploration of carry speculation mechanisms
ST2 adders
  Speculative, guarantee correctness
  Save 75-87% of adder energy, outperform state-of-the-art by 67%
ST2 GPU
  Integrate ST2 adders into GPU warp pipeline
  Reduces GPU chip energy consumption by 21%
  Practically no impact on performance and area
ST2 GPU Contributions
Notes: To tackle these, we present ST2 GPU.
We observe and quantify a new type of correlation we call spatio-temporal value correlation. We use this insight to develop a practical, high-performance carry speculation unit for sliced adders.
We propose ST2 adders which are voltage-scaled sliced speculative adders that engage dynamic carry speculation only when absolutely necessary.
ST2 adders guarantee correctness and outperform state-of-the-art designs.
We also propose ST2 GPU, an architecture that integrates ST2 adders and their carry speculation unit into the GPU warp pipeline
Finally, we show that ST2 GPU achieves significant power savings with negligible overheads.

## Slide 13
for (int i=0; i < iteration ; i++) {
...
if ( (tx>=(i+1) && (tx<=(BLOCK_SIZE-2-i)) ) && isValid) {
...
int shortest = MIN(left, up);
shortest = MIN(shortest, right);
int index = cols*(startStep+i)+xidx;
result[tx] = shortest + gpuWall[index];
}
...
}
“Hot” loop in a real-world GPU workload, Pathfinder:
How to Predict Carry Chains?
Notes: So, how can we predict carry chains?
Let’s take a look at the hot loop in a real-world GPU workload called pathfinder.

## Slide 14
for (int i=0; i < iteration ; i++) {
...
if ( (tx>=(i+1) && (tx<=(BLOCK_SIZE-2-i)) ) && isValid) {
...
int shortest = MIN(left, up);
shortest = MIN(shortest, right);
int index = cols*(startStep+i)+xidx;
result[tx] = shortest + gpuWall[index];
}
...
}
PC1
PC2
PC3
PC4
PC5
PC6
PC7
“Hot” loop in a real-world GPU workload, Pathfinder:
How to Predict Carry Chains?
Notes: Each one of the operations we enclose in boxes performs an addition.
We mark each one of these additions with their logical Program Counter ranging from PC1 to PC7.

## Slide 15
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140
PC1 | 165 | 164 | 163 | 162 | 161 | 160 | 159 | 158 | 157 | 156 | 155 | 154 | 153 | 152 | 151 | 150 | 149 | 148 | 147 | 146
PC2 | 254 | 253 | 252 | 251 | 250 | 249 | 248 | 247 | 246 | 245 | 244 | 243 | 242 | 241 | 240 | 239 | 238 | 237 | 236 | 235
PC3 | -94 | -95 | -96 | -97 | -98 | -99 | -100 | -101 | -102 | -103 | -104 | -105 | -106 | -107 | -108 | -109 | -110 | -111 | -112 | -113
PC4 | -5 | -2 | -3 | -5 | 0 | -1 | 0 | 6 | -2 | 2 | 5 | -1 | 5 | -3 | -6 | -1 | -5 | 1 | -2 | -14
PC5 | 0 | -3 | -1 | -7 | 0 | 0 | -3 | -5 | -8 | 0 | -2 | 0 | 0 | 0 | -4 | 0 | -6 | 0 | -2 | -4
PC6 | 90000 | 190000 | 290000 | 390000 | 490000 | 590000 | 690000 | 790000 | 890000 | 990000 | 1090000 | 1190000 | 1290000 | 1390000 | 1490000 | 1590000 | 1690000 | 1790000 | 1890000 | 1990000
PC7 | 9 | 13 | 12 | 16 | 13 | 8 | 10 | 13 | 17 | 18 | 25 | 21 | 24 | 24 | 24 | 30 | 31 | 38 | 45 | 37
Chart: Logical Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 165 | 254 | -94 | -5 | 0 | 90000 | 9
iteration 1
Arithmetic Op. Result
How to Predict Carry Chains?
Notes: Now let's look at the result of these arithmetic operations during the first loop iteration.
This plot shows the value calculated by each addition shown in the previous slide, color-coded to distinguish each add instruction.
The values generated by these additions as they execute in time order vary greatly.

## Slide 16
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140
PC1 | 165 | 164 | 163 | 162 | 161 | 160 | 159 | 158 | 157 | 156 | 155 | 154 | 153 | 152 | 151 | 150 | 149 | 148 | 147 | 146
PC2 | 254 | 253 | 252 | 251 | 250 | 249 | 248 | 247 | 246 | 245 | 244 | 243 | 242 | 241 | 240 | 239 | 238 | 237 | 236 | 235
PC3 | -94 | -95 | -96 | -97 | -98 | -99 | -100 | -101 | -102 | -103 | -104 | -105 | -106 | -107 | -108 | -109 | -110 | -111 | -112 | -113
PC4 | -5 | -2 | -3 | -5 | 0 | -1 | 0 | 6 | -2 | 2 | 5 | -1 | 5 | -3 | -6 | -1 | -5 | 1 | -2 | -14
PC5 | 0 | -3 | -1 | -7 | 0 | 0 | -3 | -5 | -8 | 0 | -2 | 0 | 0 | 0 | -4 | 0 | -6 | 0 | -2 | -4
PC6 | 90000 | 190000 | 290000 | 390000 | 490000 | 590000 | 690000 | 790000 | 890000 | 990000 | 1090000 | 1190000 | 1290000 | 1390000 | 1490000 | 1590000 | 1690000 | 1790000 | 1890000 | 1990000
PC7 | 9 | 13 | 12 | 16 | 13 | 8 | 10 | 13 | 17 | 18 | 25 | 21 | 24 | 24 | 24 | 30 | 31 | 38 | 45 | 37
Chart: Logical Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 165 | 254 | -94 | -5 | 0 | 90000 | 9
iteration 1
Arithmetic Op. Result
Temporal Correlation is not enough!
How to Predict Carry Chains?
Notes: Thus, using only temporal history will result in poor carry speculation accuracy.

## Slide 17
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140
PC1 | 165 | 164 | 163 | 162 | 161 | 160 | 159 | 158 | 157 | 156 | 155 | 154 | 153 | 152 | 151 | 150 | 149 | 148 | 147 | 146
PC2 | 254 | 253 | 252 | 251 | 250 | 249 | 248 | 247 | 246 | 245 | 244 | 243 | 242 | 241 | 240 | 239 | 238 | 237 | 236 | 235
PC3 | -94 | -95 | -96 | -97 | -98 | -99 | -100 | -101 | -102 | -103 | -104 | -105 | -106 | -107 | -108 | -109 | -110 | -111 | -112 | -113
PC4 | -5 | -2 | -3 | -5 | 0 | -1 | 0 | 6 | -2 | 2 | 5 | -1 | 5 | -3 | -6 | -1 | -5 | 1 | -2 | -14
PC5 | 0 | -3 | -1 | -7 | 0 | 0 | -3 | -5 | -8 | 0 | -2 | 0 | 0 | 0 | -4 | 0 | -6 | 0 | -2 | -4
PC6 | 90000 | 190000 | 290000 | 390000 | 490000 | 590000 | 690000 | 790000 | 890000 | 990000 | 1090000 | 1190000 | 1290000 | 1390000 | 1490000 | 1590000 | 1690000 | 1790000 | 1890000 | 1990000
PC7 | 9 | 13 | 12 | 16 | 13 | 8 | 10 | 13 | 17 | 18 | 25 | 21 | 24 | 24 | 24 | 30 | 31 | 38 | 45 | 37
Chart: Logical Time
iteration 1
iteration 2
iteration 3
iteration 4
Arithmetic Op. Result
How to Predict Carry Chains?
Notes: However, the values produced by the same instruction across iterations are of similar magnitude and are strongly correlated.

## Slide 18
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140
PC1 | 165 | 164 | 163 | 162 | 161 | 160 | 159 | 158 | 157 | 156 | 155 | 154 | 153 | 152 | 151 | 150 | 149 | 148 | 147 | 146
PC2 | 254 | 253 | 252 | 251 | 250 | 249 | 248 | 247 | 246 | 245 | 244 | 243 | 242 | 241 | 240 | 239 | 238 | 237 | 236 | 235
PC3 | -94 | -95 | -96 | -97 | -98 | -99 | -100 | -101 | -102 | -103 | -104 | -105 | -106 | -107 | -108 | -109 | -110 | -111 | -112 | -113
PC4 | -5 | -2 | -3 | -5 | 0 | -1 | 0 | 6 | -2 | 2 | 5 | -1 | 5 | -3 | -6 | -1 | -5 | 1 | -2 | -14
PC5 | 0 | -3 | -1 | -7 | 0 | 0 | -3 | -5 | -8 | 0 | -2 | 0 | 0 | 0 | -4 | 0 | -6 | 0 | -2 | -4
PC6 | 90000 | 190000 | 290000 | 390000 | 490000 | 590000 | 690000 | 790000 | 890000 | 990000 | 1090000 | 1190000 | 1290000 | 1390000 | 1490000 | 1590000 | 1690000 | 1790000 | 1890000 | 1990000
PC7 | 9 | 13 | 12 | 16 | 13 | 8 | 10 | 13 | 17 | 18 | 25 | 21 | 24 | 24 | 24 | 30 | 31 | 38 | 45 | 37
Chart: Logical Time
iteration 1
iteration 2
iteration 3
iteration 4
Arithmetic Op. Result
Spatio-Temporal Value Correlation
How to Predict Carry Chains?
Notes: If we look, for example, at the values generated by the instruction at PC2 across iterations, in time order, we observe that they are very close to each other.
We call this spatio-temporal value correlation.
Next, we’re going to quantify the effect of this on carry speculation accuracy.

## Slide 19
Chart: Carry Pred. Accuracy
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Average
Prev + Gtid | 0.27133 | 0.46656 | 0.8554 | 0.3739 | 0.20363 | 0.45231 | 0.47974 | 0.63138 | 0.61105 | 0.49348 | 0.53586 | 0.34412 | 0.44454 | 0.95084 | 0.48732 | 0.54777 | 0.39345 | 0.38313 | 0.58784 | 0.4538 | 0.46215 | 0.42604 | 0.62274 | 0.49906
Prev + FullPC + Gtid
Prev + FullPC + Ltid
Temporal
Correlation:
50%
Quantifying Spatio-Temporal Value Correlation
Notes: Instead of a monolithic 64-bit adder, let’s look at additions as performed by stringing together 8-bit adder slices.
Each slice is fed with the carry out of the previous 8-bit slice.
Comparing carry-ins between consecutive additions executed within each GPU thread results in 50% carry-in matches on average.
Thus, there is practically no correlation along the temporal axis alone.

## Slide 20
Chart: Carry Pred. Accuracy
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Average
Prev + Gtid | 0.27133 | 0.46656 | 0.8554 | 0.3739 | 0.20363 | 0.45231 | 0.47974 | 0.63138 | 0.61105 | 0.49348 | 0.53586 | 0.34412 | 0.44454 | 0.95084 | 0.48732 | 0.54777 | 0.39345 | 0.38313 | 0.58784 | 0.4538 | 0.46215 | 0.42604 | 0.62274 | 0.49906
Prev + FullPC + Gtid | 0.87227 | 0.69132 | 0.8512 | 0.74238 | 0.99089 | 0.83942 | 0.90012 | 0.54461 | 0.84571 | 0.81655 | 0.87579 | 0.79372 | 0.83262 | 0.97585 | 0.82786 | 0.86698 | 0.68363 | 0.90349 | 0.89465 | 0.91882 | 0.71952 | 0.85049 | 0.91107 | 0.83256
Prev + FullPC + Ltid
Spatio-Temporal
Temporal
Correlation:
83%
Quantifying Spatio-Temporal Value Correlation
Notes: However, when we compare separately the carry-ins from consecutive executions with the same Program Counter within each GPU thread, we get 83% carry-in matches.
Thus, spatio-temporal correlation between carry chains is strong.

## Slide 21
Chart: Carry Pred. Accuracy
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Average
Prev + Gtid | 0.27133 | 0.46656 | 0.8554 | 0.3739 | 0.20363 | 0.45231 | 0.47974 | 0.63138 | 0.61105 | 0.49348 | 0.53586 | 0.34412 | 0.44454 | 0.95084 | 0.48732 | 0.54777 | 0.39345 | 0.38313 | 0.58784 | 0.4538 | 0.46215 | 0.42604 | 0.62274 | 0.49906
Prev + FullPC + Gtid | 0.87227 | 0.69132 | 0.8512 | 0.74238 | 0.99089 | 0.83942 | 0.90012 | 0.54461 | 0.84571 | 0.81655 | 0.87579 | 0.79372 | 0.83262 | 0.97585 | 0.82786 | 0.86698 | 0.68363 | 0.90349 | 0.89465 | 0.91882 | 0.71952 | 0.85049 | 0.91107 | 0.83256
Prev + FullPC + Ltid
Spatio-Temporal
Temporal
Correlation:
Challenging to implement!
Per-thread bookkeeping
2048 threads / SM
83%
Quantifying Spatio-Temporal Value Correlation
Notes: It is important to note that modern GPUs support up to 2048 threads per SM and a per-thread history will be challenging to implement due to area overheads.

## Slide 22
Chart: Carry Pred. Accuracy
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Average
Prev + Gtid | 0.27133 | 0.46656 | 0.8554 | 0.3739 | 0.20363 | 0.45231 | 0.47974 | 0.63138 | 0.61105 | 0.49348 | 0.53586 | 0.34412 | 0.44454 | 0.95084 | 0.48732 | 0.54777 | 0.39345 | 0.38313 | 0.58784 | 0.4538 | 0.46215 | 0.42604 | 0.62274 | 0.49906
Prev + FullPC + Gtid | 0.87227 | 0.69132 | 0.8512 | 0.74238 | 0.99089 | 0.83942 | 0.90012 | 0.54461 | 0.84571 | 0.81655 | 0.87579 | 0.79372 | 0.83262 | 0.97585 | 0.82786 | 0.86698 | 0.68363 | 0.90349 | 0.89465 | 0.91882 | 0.71952 | 0.85049 | 0.91107 | 0.83256
Prev + FullPC + Ltid | 0.82472 | 0.93008 | 0.99409 | 0.75248 | 0.99671 | 0.99513 | 0.95205 | 0.55618 | 0.90113 | 0.83609 | 0.92043 | 0.91497 | 0.89831 | 0.99037 | 0.88848 | 0.86796 | 0.79833 | 0.93962 | 0.90886 | 0.82515 | 0.89074 | 0.88509 | 0.99538 | 0.88967
Spatio-Temporal Shared-Thread
Spatio-Temporal
Temporal
Correlation:
89%
Quantifying Spatio-Temporal Value Correlation
Notes: We can fix this problem by allowing some form of history-sharing between threads. Threads in GPUs execute in bunches of 32, called warps.
By allowing such sharing between threads in the same lane across different warps, we not only makes the design practical, but also increase accuracy to 89%. This is because threads can now learn faster by sharing history across warps.
We capitalize on spatio-temporal value correlation to design the ST2 carry speculation unit.
Let’s first traverse the design space of carry speculation to see how we arrive at our design.

## Slide 23
Unsurprisingly, a static zero speculation suffers high error rates (static one is much worse)
Chart: Avg. Thread Misprediction Rate
| staticZero
Average Thread Misprediction Rate | 0.36374
Exploring Carry Speculation Mechanisms
Notes: At first, the simplest carry speculation one can do is static: That is, always predict 0.
Unsurprisingly, this suffers high error rates.

## Slide 24
VaLHALLA (state-of-the-art): reduce mispredictions via dynamic speculation
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA
Average Thread Misprediction Rate | 0.36374 | 0.2724
25% reduction
not always necessary
Exploring Carry Speculation Mechanisms
Notes: The current state-of-the-art design, VaLHALLA, reduces the misprediction rate to 27% by enforcing dynamic speculation.
Now, this dynamic speculation is not always necessary.

## Slide 25
Peek at MSb of input to previous slice to make static prediction; dynamic prediction used only when static not possible
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA | VALHALLA + Peek
Average Thread Misprediction Rate | 0.36374 | 0.2724 | 0.22335
Exploring Carry Speculation Mechanisms
Still based on VaLHALLA: broadcasts same single-bit prediction to all slices
Notes: If the most significant bits of the two previous slice inputs are both zeroes, then the carry-in will surely be zero.
If they are both ones, then the carry-in will surely be one.
Such static predictions are guaranteed correct, and we only need dynamic prediction when static predictions are not possible.
In this design, the dynamic prediction is still based on VaLHALLA, which is a broadcast of the same single-bit prediction to all slices.

## Slide 26
Instead, predict carry per slice using previous history (last arithmetic op.) (temporal correlation)
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA | VALHALLA + Peek | Prev + Peek
Average Thread Misprediction Rate | 0.36374 | 0.2724 | 0.22335 | 0.20208
But, temporal correlation alone is not enough
Exploring Carry Speculation Mechanisms
Notes: Switching to predict a carry for each slice using previous history lowers the misprediction rate to 20%.
Note that we are using only temporal correlation here which alone isn’t enough as we’ve seen before.

## Slide 27
Spatio-temporal correlation: keep history of last 2k arithmetic operations (use lowest k PC bits in history table index—ModPCk)
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA | VALHALLA + Peek | Prev + Peek | Prev + ModPC1 + Peek | Prev + ModPC2 + Peek | Prev + ModPC3 + Peek | Prev + ModPC4 + Peek
Average Thread Misprediction Rate | 0.36374 | 0.2724 | 0.22335 | 0.20208 | 0.18004 | 0.16497 | 0.14072 | 0.11661
Exploring Carry Speculation Mechanisms
remember 2 PCs
remember 4 PCs
remember 8 PCs
remember 16 PCs
Notes: We can add a spatial dimension to our history by remembering the history of the last 2^k arithmetic operations.
When k is 4, the misprediction rate drops to 11.6%.

## Slide 28
Spatio-temporal correlation: keep history of last 2k arithmetic operations (use lowest k PC bits in history table index—ModPCk)
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA | VALHALLA + Peek | Prev + Peek | Prev + ModPC1 + Peek | Prev + ModPC2 + Peek | Prev + ModPC3 + Peek | Prev + ModPC4 + Peek
Average Thread Misprediction Rate | 0.36374 | 0.2724 | 0.22335 | 0.20208 | 0.18004 | 0.16497 | 0.14072 | 0.11661
57% reduction
Exploring Carry Speculation Mechanisms
Impractical to implement
Notes: However, this design is impractical to implement.
If there is only one history for all threads, it will be stored in a *centralized* location and there will be high contention to read and write from 1000’s of threads.
The performance implications of this design may slow down the entire execution.

## Slide 29
Use global thread ID to keep per-thread history
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA | VALHALLA + Peek | Prev + Peek | Prev + ModPC1 + Peek | Prev + ModPC2 + Peek | Prev + ModPC3 + Peek | Prev + ModPC4 + Peek | Gtid + Prev + ModPC4 + Peek
Average Thread Misprediction Rate | 0.36374 | 0.2724 | 0.22335 | 0.20208 | 0.18004 | 0.16497 | 0.14072 | 0.11661 | 0.24675
Low performance + challenging to implement!
Per-thread bookkeeping
2048 threads / SM
Exploring Carry Speculation Mechanisms
Notes: To fix this issue, we can use global thread ID to keep per-thread history.
This is possible to implement but requires too much storage for history.
It also performs badly in comparison to the designs we’ve seen until now.

## Slide 30
Keep per-thread history in warp (use Local thread ID); share across warps. Sharing history across warps increases accuracy
Chart: Avg. Thread Misprediction Rate
| staticZero | VaLHALLA | VALHALLA + Peek | Prev + Peek | Prev + ModPC1 + Peek | Prev + ModPC2 + Peek | Prev + ModPC3 + Peek | Prev + ModPC4 + Peek | Gtid + Prev + ModPC4 + Peek | Ltid + Prev + ModPC4 + Peek
Average Thread Misprediction Rate | 0.36374 | 0.2724 | 0.22335 | 0.20208 | 0.18004 | 0.16497 | 0.14072 | 0.11661 | 0.24675 | 0.090704
67% reduction
ST2
Exploring Carry Speculation Mechanisms
Notes: To reduce area overheads, we can allow history-sharing between threads by keeping per-thread history only within warps.
This makes the design practical and also lowers misprediction rate because threads now learn faster by sharing history across warps.
This is our final design for ST2’s carry speculation unit and it achieves an average thread misprediction rate of 9% on our set of workloads.

## Slide 31
Fetch
Decode
Instruction Buffer
Scoreboard
Functional Units
SFUs, MULs, DIVs
LD/ST Units
FPUs
ALUs
Fetch
Decode
Issue
Register Read
Execute
Write-Back
Release
Ready
ALUs
FPUs (FP32, FP64)
LD/ST Units
SFUs, MULs, DIVs
Warp Scheduler
Instruction Cache
Register File - Write
Register File - Read
GPU SM Pipeline Design
Notes: Here’s the baseline GPU SM pipeline design.

## Slide 32
Stall
Fetch
Decode
Instruction Buffer
Scoreboard
Carry Register File - Write
Functional Units
SFUs, MULs, DIVs
LD/ST Units
FPUs
ALUs
Fetch
Decode
Issue
Register Read
Execute
Write-Back
Release
Ready
ALUs
FPUs (FP32, FP64)
LD/ST Units
SFUs, MULs, DIVs
Warp Scheduler
Instruction Cache
Register File - Write
Register File - Read
Carry Register File - Read
Stall
Level-Up Voltage Shifters
Level-Down Voltage Shifters
ST2 GPU SM Pipeline Design
Notes: Now let’s look at our proposed GPU SM pipeline modifications to support ST2.
A carry register file provides speculated carry-ins which are read along with regular register file operands during the register read pipeline stage.
These carry-ins are sent to the warp’s Functional units during the execute stage and are then utilized by ST2 adders to perform the computation.
Upon completion, threads with mispredictions will update the carry register file at the write-back pipeline stage similarly to a register file update.
We need an extra cycle for mispredictions, so we add a stall signal to hold the scheduling of the next instruction if necessary.

## Slide 33
Stall
Fetch
Decode
Instruction Buffer
Scoreboard
Carry Register File - Write
Functional Units
SFUs, MULs, DIVs
LD/ST Units
FPUs
ALUs
Fetch
Decode
Issue
Register Read
Execute
Write-Back
Release
Ready
ALUs
FPUs (FP32, FP64)
LD/ST Units
SFUs, MULs, DIVs
Warp Scheduler
Instruction Cache
Register File - Write
Register File - Read
Carry Register File - Read
Stall
Level-Up Voltage Shifters
Level-Down Voltage Shifters
ST2 GPU SM Pipeline Design
Notes: Now let’s look at the internal structure of the carry register file and the warp functional units.

## Slide 34
Carry Register [15]
Carry Register [14]
Carry Register [0]
224 Bits
PC[3:0]
Cpred[223:0]
Slice 0
Slice 1
Slice 2
Slice 3
Slice 4
Slice 5
Slice 6
Slice 7
Slice 0
Slice 1
Slice 2
Slice 3
Slice 4
Slice 5
Slice 6
Slice 7
Thread 31
Thread 30
Thread 0
Cpred[223:217]
Cpred[216:210]
Cpred[6:0]
Slice 0
Slice 1
Slice 2
Slice 3
Slice 4
Slice 5
Slice 6
Slice 7
Mux
Previous Carry History Table
ST2 Carry Speculation Unit Design
Notes: Since all threads in a warp run together, we make a prediction concurrently for all threads in a warp.
All 32 threads in the warp need a 1-bit carry prediction per slice except slice 0. Thus, each line in the history table is 224 bits long.
The history table has 16 such entries and is indexed by the lowest 4 Program Counter bits.

## Slide 35
Carry Register [15]
Carry Register [14]
Carry Register [0]
224 Bits
PC[3:0]
Cpred[223:0]
Slice 0
Slice 1
Slice 2
Slice 3
Slice 4
Slice 5
Slice 6
Slice 7
Slice 0
Slice 1
Slice 2
Slice 3
Slice 4
Slice 5
Slice 6
Slice 7
Thread 31
Thread 30
Thread 0
Cpred[223:217]
Cpred[216:210]
Cpred[6:0]
Slice 0
Slice 1
Slice 2
Slice 3
Slice 4
Slice 5
Slice 6
Slice 7
Mux
Previous Carry History Table
ST2 Carry Speculation Unit Design
Notes: Now let’s look at the sliced adder design for thread 0.

## Slide 36
Slice 7
Bits [63:56]
Slice 6
Bits [55:48]
Slice 5
Bits [47:40]
Slice 4
Bits [39:32]
Slice 3
Bits [31:24]
Slice 2
Bits [23:16]
Slice 1
Bits [15:8]
Slice 0
Bits [7:0]
Cin
Cout
E[1]
E[2]
E[3]
E[4]
E[5]
E[6]
E[7]
S[1]
S[2]
S[3]
S[4]
S[5]
S[6]
S[7]
Cpred[0]
Cpred[1]
Cpred[2]
Cpred[3]
Cpred[4]
Cpred[5]
Cpred[6]
ST2 Adder, Thread 0
SUB
Previous Carry History Table
ST2 Adder Design
Notes: Every slice contains an 8-bit adder and is in-charge of producing 8 bits of the 64-bit output.
Every slice except slice 0 has a similar design and can generate an error signal upon misprediction.
This error signal propagates upwards and all slices that receive the signal will recompute with the inverse carry-ins to recover from the error.
However, If a slice can perform static prediction by peeking at the previous slice’s inputs, the slice breaks the propagation of the error signal upwards.
This minimizes the number of slice recomputations that occur due to mispredictions and thus, translates to further energy savings.

## Slide 37
Slice 7
Bits [63:56]
Slice 6
Bits [55:48]
Slice 5
Bits [47:40]
Slice 4
Bits [39:32]
Slice 3
Bits [31:24]
Slice 2
Bits [23:16]
Slice 1
Bits [15:8]
Slice 0
Bits [7:0]
Cin
Cout
E[1]
E[2]
E[3]
E[4]
E[5]
E[6]
E[7]
S[1]
S[2]
S[3]
S[4]
S[5]
S[6]
S[7]
Cpred[0]
Cpred[1]
Cpred[2]
Cpred[3]
Cpred[4]
Cpred[5]
Cpred[6]
ST2 Adder, Thread 0
SUB
Previous Carry History Table
ST2 Adder Design
Notes: Let’s look at the internal design of slice 0 and slice 5.

## Slide 38
Input Register
Output Register
8-bit ADD/SUB
Cin
SUB
Cout[0]
Op2[7:0]
Op1[7:0]
Out[7:0]
Slice 0
Slice 0
Bits [7:0]
ST2 Adder Design
Notes: Slice 0 is just a regular 8-bit adder.

## Slide 39
Input Register
Output Register
8-bit ADD/SUB
Cin
SUB
Cout[0]
Op2[7:0]
Op1[7:0]
Out[7:0]
Slice 0
Input Register
Output Register
8-bit ADD/SUB
Cin
SUB
Cout[5]
Op2[47:40]
Op1[47:40]
Out[47:40]
1
0
1
0
Op2[39]
Op1[39]
1
0
Cpred[4]
Cin[5]
E[5]
Clk
S[5]
Reset
Cout DFF
state DFF
Slice 5
Cout
Slice 5
Bits [47:40]
Slice 0
Bits [7:0]
ST2 Adder Design
Notes: Apart from having an 8-bit adder in it, slice 5 contains additional logic to peek at the previous slice’s input for static prediction.
It also contains logic to support re-computations whenever necessary.
Re-computations are necessary at the end of first operation if the slice receives an error signal from previous slices, or if it detects a mismatch between the speculated carry it used to perform the first operation and the carry-out of slice 4.

## Slide 40
Synthesis: Verilog  Synopsys Design Compiler (SAED 90nm)
Circuit Simulations: Synopsys Hspice (Full Analog)
Baseline GPU Architecture: NVIDIA TITAN V Volta (GV100)
System Power Estimations: in-house GPUWattch-based power model validated against real HW (GV100)
System Performance Simulations: GPGPU-Sim 3.x in PTX simulation mode
Workloads: 9 from NVIDIA CUDA Samples, 6 from Rodinia, and 3 from Parboil
Methodology
Notes: We synthesized our designs in Synopsys Design Compiler.
We extracted netlists and performed full analog Hspice simulations to derive delay and power characteristics for the adders.
We then incorporated the relative power we derived into an in-house power simulator that models an NVIDIA Titan V Volta GPU.
For performance modeling of the same chip, we use GPGPU-Sim and run workloads from NVIDIA CUDA samples, Rodinia and Parboil benchmark suites.

## Slide 41
Power model calibrated against GV100 with 123 µbenchmarks and least-square-error solver
Validated against real silicon using HW power measurements collected from chip sensors
Average abs. relative error: 10.5%; Pearson r coefficient: 0.8 on ST2 evaluation workloads
Chart: Power Measured on Hardware (W)
| 162.583 | 135.29 | 128.32 | 107.27 | 99.078000000000003 | 98.5 | 186.399 | 122.66 | 160.09700000000001 | 138.75399999999999 | 153.327 | 161.619 | 128.50399999999999 | 154.83600000000001 | 188.09 | 133.66999999999999 | 115.42 | 125.09 | 128.41999999999999 | 140.96 | 170.07 | 117.72 | 138.24 | 90.43
 | 158.868 | 125.3884 | 117.0009 | 102.577 | 70.2028 | 93.7628 | 188.7308 | 108.5152 | 174.4176 | 183.5142 | 150.8313 | 154.1189 | 125.2552 | 138.0291 | 157.0874 | 134.5183 | 136.0262 | 130.1561 | 122.5648 | 175.9467 | 144.4547 | 87.0718 | 136.6966 | 107.6629
 | 0 | 220
Accurate Power Model, Validated Against Silicon
Notes: Our power model is calibrated against a GV100 with 123 micro-benchmarks and a least-square-error solver.
We validate our model against real silicon using hardware power measurements collected from on-chip sensors.
Our model achieves an average absolute relative error of 10.5% and pearson r coefficient of 0.8 on the workloads we use to evaluate ST2.

## Slide 42
21% GPU chip energy savings, 19% chip+DRAM savings
ST2 GPU Saves GPU System Energy
Chart: N
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Avg (intensive) | Avg (all)
ALU+FPU | 0.060223 | 0.01428 | 0.081568 | 0.020514 | 0.096782 | 0.024626 | 0.10436 | 0.032744 | 0.12734 | 0.036217 | 0.14892 | 0.035204 | 0.15311 | 0.042785 | 0.15898 | 0.028366 | 0.18769 | 0.066235 | 0.20291 | 0.060459 | 0.2117 | 0.055657 | 0.26506 | 0.081066 | 0.26766 | 0.099811 | 0.27196 | 0.066626 | 0.27327 | 0.098183 | 0.32697 | 0.098216 | 0.3513 | 0.093352 | 0.38718 | 0.10607 | 0.45275 | 0.13437 | 0.50986 | 0.15748 | 0.51867 | 0.17643 | 0.54965 | 0.15098 | 0.54965 | 0.20539 | 0.36815 | 0.11315 | 0.27274 | 0.08196
int Mul/Div | 1.5181e-05 | 1.5181e-05 | 0.0048119 | 0.0048119 | 0.021693 | 0.021693 | 0.011577 | 0.011577 | 0.017137 | 0.017137 | 0.016689 | 0.016689 | 0.045752 | 0.045752 | 0.011334 | 0.011334 | 0.0067475 | 0.0067475 | 0.0041643 | 0.0041643 | 0.031634 | 0.031634 | 0.1052 | 0.1052 | 0.061074 | 0.061074 | 0.0033254 | 0.0033254 | 0.049789 | 0.049789 | 0.00043704 | 0.00043704 | 0.011402 | 0.011402 | 0.010604 | 0.010604 | 0.00061128 | 0.00061128 | 0.0041512 | 0.0041512 | 0.011435 | 0.011435 | 0.00039316 | 0.00039316 | 0.0057732 | 0.0057732 | 0.021428 | 0.021428 | 0.018946 | 0.018946
fp Mul/Div | 0.48104 | 0.48104 | 0.020893 | 0.020893 | 0.25183 | 0.25183 | 2.517e-09 | 2.517e-09 | 0.20524 | 0.20524 | 0.04044 | 0.04044 | 0.22603 | 0.22603 | 0.077114 | 0.077114 | 0 | 0 | 0 | 0 | 0.2026 | 0.2026 | 0.020976 | 0.020976 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0087237 | 0.0087237 | 0 | 0 | 0.0053788 | 0.0053788 | 0.016977 | 0.016977 | 0.066968 | 0.066968
Chart: Norm. System Energy
| Base | ST2 |  | Base | ST2 |  | Base | ST2 |  | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 | Base | ST2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
ALU+FPU | 0.060223 | 0.01428 | 0.081568 | 0.020514 | 0.096782 | 0.024626 | 0.10436 | 0.032744 | 0.12734 | 0.036217 | 0.14892 | 0.035204 | 0.15311 | 0.042785 | 0.15898 | 0.028366 | 0.18769 | 0.066235 | 0.20291 | 0.060459 | 0.2117 | 0.055657 | 0.26506 | 0.081066 | 0.26766 | 0.099811 | 0.27196 | 0.066626 | 0.27327 | 0.098183 | 0.32697 | 0.098216 | 0.3513 | 0.093352 | 0.38718 | 0.10607 | 0.45275 | 0.13437 | 0.50986 | 0.15748 | 0.51867 | 0.17643 | 0.54965 | 0.15098 | 0.54965 | 0.20539 | 0.36815 | 0.11315 | 0.27274 | 0.08196
int Mul/Div | 1.5181e-05 | 1.5181e-05 | 0.0048119 | 0.0048119 | 0.021693 | 0.021693 | 0.011577 | 0.011577 | 0.017137 | 0.017137 | 0.016689 | 0.016689 | 0.045752 | 0.045752 | 0.011334 | 0.011334 | 0.0067475 | 0.0067475 | 0.0041643 | 0.0041643 | 0.031634 | 0.031634 | 0.1052 | 0.1052 | 0.061074 | 0.061074 | 0.0033254 | 0.0033254 | 0.049789 | 0.049789 | 0.00043704 | 0.00043704 | 0.011402 | 0.011402 | 0.010604 | 0.010604 | 0.00061128 | 0.00061128 | 0.0041512 | 0.0041512 | 0.011435 | 0.011435 | 0.00039316 | 0.00039316 | 0.0057732 | 0.0057732 | 0.021428 | 0.021428 | 0.018946 | 0.018946
fp Mul/Div | 0.48104 | 0.48104 | 0.020893 | 0.020893 | 0.25183 | 0.25183 | 2.517e-09 | 2.517e-09 | 0.20524 | 0.20524 | 0.04044 | 0.04044 | 0.22603 | 0.22603 | 0.077114 | 0.077114 | 0 | 0 | 0 | 0 | 0.2026 | 0.2026 | 0.020976 | 0.020976 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0087237 | 0.0087237 | 0 | 0 | 0.0053788 | 0.0053788 | 0.016977 | 0.016977 | 0.066968 | 0.066968
SFU | 0.00070362 | 0.00070362 | 0 | 0 | 0 | 0 | 0 | 0 | 0.20524 | 0.20524 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.014865 | 0.014865 | 0.080675 | 0.080675 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0068243 | 0.0068243 | 0.013108 | 0.013108
RegFile | 0.3623 | 0.3623 | 0.059568 | 0.059568 | 0.29861 | 0.29861 | 0.05195 | 0.05195 | 0.21654 | 0.21654 | 0.065863 | 0.065863 | 0.090115 | 0.090115 | 0.12239 | 0.12239 | 0.10263 | 0.10263 | 0.13536 | 0.13536 | 0.16688 | 0.16688 | 0.14639 | 0.14639 | 0.12457 | 0.12457 | 0.13958 | 0.13958 | 0.12778 | 0.12778 | 0.16501 | 0.16501 | 0.16482 | 0.16482 | 0.16683 | 0.16683 | 0.23003 | 0.23003 | 0.2909 | 0.2909 | 0.19504 | 0.19504 | 0.24583 | 0.24583 | 0.23141 | 0.23141 | 0.18075 | 0.18075 | 0.16958 | 0.16958
Caches+MC | 0.037825 | 0.037825 | 0.04818 | 0.04818 | 0.18318 | 0.18318 | 0.11478 | 0.11478 | 0.15453 | 0.15453 | 0.13129 | 0.13129 | 0.1123 | 0.1123 | 0.18606 | 0.18606 | 0.089553 | 0.089553 | 0.17151 | 0.17151 | 0.052463 | 0.052463 | 0.11745 | 0.11745 | 0.14328 | 0.14328 | 0.081068 | 0.081068 | 0.13846 | 0.13846 | 0.11134 | 0.11134 | 0.10483 | 0.10483 | 0.055085 | 0.055085 | 0.11907 | 0.11907 | 0.05608 | 0.05608 | 0.073378 | 0.073378 | 0.059886 | 0.059886 | 0.02274 | 0.02274 | 0.093332 | 0.093332 | 0.1028 | 0.1028
NoC | 0.00017039 | 0.00017039 | 0.20961 | 0.20961 | 0.077206 | 0.077206 | 0.3682 | 0.3682 | 0.0039619 | 0.0039619 | 0.32246 | 0.32246 | 0.29397 | 0.29397 | 0.35016 | 0.35016 | 0.26848 | 0.26848 | 0.23773 | 0.23773 | 0.2466 | 0.2466 | 0.17983 | 0.17983 | 0.22032 | 0.22032 | 0.17922 | 0.17922 | 0.22992 | 0.22992 | 0.21065 | 0.21065 | 0.18135 | 0.18135 | 0.14686 | 0.14686 | 0.077823 | 0.077823 | 0.084731 | 0.084731 | 0.14166 | 0.14166 | 0.050058 | 0.050058 | 0.085548 | 0.085548 | 0.16231 | 0.16231 | 0.18115 | 0.18115
Others | 0.05771 | 0.05771 | 0.073042 | 0.073042 | 0.05314 | 0.05314 | 0.053108 | 0.053108 | 0.067511 | 0.067511 | 0.045573 | 0.045573 | 0.060368 | 0.060368 | 0.093972 | 0.093972 | 0.14954 | 0.14954 | 0.059097 | 0.059097 | 0.072273 | 0.072273 | 0.046241 | 0.046241 | 0.057541 | 0.057541 | 0.047109 | 0.047109 | 0.052722 | 0.052722 | 0.041473 | 0.041473 | 0.041763 | 0.041763 | 0.045246 | 0.045246 | 0.058519 | 0.058519 | 0.05043 | 0.05043 | 0.049402 | 0.049402 | 0.054837 | 0.054837 | 0.083113 | 0.083113 | 0.054269 | 0.054269 | 0.061467 | 0.061467
DRAM | 1.6975e-05 | 1.6975e-05 | 0.50232 | 0.50232 | 0.017551 | 0.017551 | 0.29603 | 0.29603 | 0.0024936 | 0.0024936 | 0.22877 | 0.22877 | 0.018355 | 0.018355 | 3.0092e-06 | 3.0092e-06 | 0.19535 | 0.19535 | 0.18923 | 0.18923 | 0.00097786 | 0.00097786 | 0.038189 | 0.038189 | 0.12555 | 0.12555 | 0.27774 | 0.27774 | 0.12806 | 0.12806 | 0.14412 | 0.14412 | 0.14454 | 0.14454 | 0.18819 | 0.18819 | 0.061188 | 0.061188 | 0.0038465 | 0.0038465 | 0.0016973 | 0.0016973 | 0.039346 | 0.039346 | 0.00082554 | 0.00082554 | 0.095964 | 0.095964 | 0.11323 | 0.11323
ALU+FPU Intensive: >20% ALU+FPU System Energy
70% ALU+FPU energy savings
Notes: Here’s the normalized energy breakdowns for both the baseline and ST2 GPU architectures as reported by our power model.
The application kernels shown here are in the order of increasing arithmetic intensity.
On average, ALUs and FPUs consume 27.3% of total energy on the baseline chip.
ST2 reduces the power consumption of these units by 70% and achieves 21% chip energy savings, that’s 19% energy savings if we include the off-chip DRAM.

## Slide 43
Chart: Norm. Execution Time
| binomial | kmeans_K1 | sgemm | walsh_K1 | mri-q_K1 | bprop_K2 | sradv1_K1 | dct8x8_K1 | dwt2d_K1 | sortNets_K1 | qrng_K2 | bprop_K1 | b+tree_K1 | histo_K1 | b+tree_K2 | msort_K1 | walsh_K2 | pathfinder | sortNets_K2 | sad_K1 | sobolQrng | msort_K2 | qrng_K1 | Average
Execution Time (Normalized) | 1.0014 | 1.0032 | 0.99898 | 0.99692 | 1.0001 | 1.0131 | 1.0025 | 0.91019 | 1.0353 | 0.9994 | 0.98784 | 0.99477 | 1.0047 | 0.98415 | 1.0046 | 1.0028 | 1.0009 | 0.99928 | 1.0018 | 0.96459 | 1.0115 | 0.99888 | 1 | 0.99638
We Don’t Affect Performance
Notes: These energy savings come with practically no performance overhead.
We rarely mis-predict and even when we do, it doesn’t matter much for performance.

## Slide 44
Storage: 50KB, i.e., 0.09% of on-chip caches and register file area
  448-BYTE CRF (16 x 224 bits) per SM  35KB
  2 bits for state and Count DFFs per slice  15KB
Voltage shifters: <0.68% Volta GV100 chip area
Less Than 0.75% Area Overhead
Notes: The energy savings also come with a negligible area overhead.
The area required for the carry register file is about 0.1% of the on-chip cache and register file area.
Additionally, the area overhead for voltage shifters is about 0.7% of the GV100 chip area.

## Slide 45
Spatio-temporal value correlation
Design-space exploration
  Winner: spatio-temporal history + history sharing + disciplined static predictions
ST2 adders
  Speculative, guarantee correctness
  Save 75-87% of adder energy, outperform state-of-the-art by 67%
ST2 GPU
  Integrate ST2 adders into GPU warp pipeline
  Reduces GPU chip energy consumption by 21%
  Practically no impact on performance and area
Conclusions
Notes: In conclusion,
We quantify spatio-temporal value correlation and use it to develop a practical, high-performance carry speculation unit for sliced adders.
ST2 adders are voltage-scaled sliced speculative adders that guarantee correctness and outperform state-of-the-art by 67% on speculation accuracy.
We propose ST2 GPU, an architecture that integrates ST2 adders and their carry speculation unit into the GPU warp pipeline.
Finally, we show that ST2 GPU achieves 21% chip energy savings with negligible performance and area overheads.

## Slide 46
Spatio-temporal value correlation
Design-space exploration
  Winner: spatio-temporal history + history sharing + disciplined static predictions
ST2 adders
  Speculative, guarantee correctness
  Save 75-87% of adder energy, outperform state-of-the-art by 67%
ST2 GPU
  Integrate ST2 adders into GPU warp pipeline
  Reduces GPU chip energy consumption by 21%
  Practically no impact on performance and area
THANK YOU!
Questions?
Conclusions
Notes: Thank you for listening.