## Slide 1: An Overview of Software-Defined Network
Presenter: Xitao Wen

## Slide 2: Review: How a Router Works
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
* Copied from slides of EECS 340

## Slide 3: Inside a Router
Routing Engine
Packet Forwarding Fabric
Input Ports
Output Ports
General-purpose CPU
ASIC, or specialized chips

## Slide 8: Experimenter’s Dream (Vendor’s Nightmare)
Standard
Network
Processing
hw
sw
Experimenter writes experimental code on switch/router
User-
defined
Processing

## Slide 9: Furthermore, we want…
Isolation: Regular production traffic untouched
Virtualized and programmable: Different flows processed in different ways
Equipment we can trust in our wiring closet
Open development environment for all researchers (e.g. Linux, Verilog, etc).
Flexible definitions of a flow
  Individual application traffic
  Aggregated flows
  Alternatives to IP running side-by-side
  …

## Slide 13: Software-Defined Network

## Slide 14: OpenFlow Architecture
Routing Engine
Packet Forwarding Fabric
Input Ports
Output Ports
Switch
Controller
Network Protocol over SSL

## Slide 15: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 16: Step 1: Separate Control from Datapath

## Slide 17: Step 2: Cache flow decisions in datapath

## Slide 18: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 19: OpenFlow Switch Model
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
SSL
hw
sw
OpenFlow Switch specification

## Slide 20: OpenFlow Switch Model
Hardware
  One or more flow tables
  Group table (since Spec 1.1)
Software
  Secure Channel

## Slide 21: Flow Table Entry
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Matcher
Action
Counters
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Rewrite headers
Map to queue
+ mask
Packet + byte counters

## Slide 24: Secure Channel
SSL Connection, site-specific key
Controller discovery protocol
Encapsulate packets for controller
Send link/port state to controller

## Slide 25: Current OpenFlow Hardware

## Slide 26: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 27: OpenFlow Protocol
Connection
  Hello, Echo, Feature, Config…
Read-State
  Statistics, Port-status, Error
Modify-State
  Flow, Group, Config
Packet-in/Packet-out
Barrier

## Slide 28: Reactive vs. Proactive (pre-populated)

## Slide 29: Reactive Flow-Push

## Slide 30: Proactive Flow-Push

## Slide 31: Evolving Protocol

## Slide 32: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 33: Key Task of OF Controller
OpenFlow protocol is largely deltas:
  Switch-to-Controller: changes of network state
  Controller-to-Switch: changes of configuration
It is a natural way to write control logic

## Slide 34: Architectural View: Network OS
OF Controller
Operating System
App
App
App
App
Switch
Switch
Switch

## Slide 35: Open Controllers

## Slide 36: Open Controllers (2)

## Slide 37: NOX: A Bit of History
NOX was the first SDN controller
Released under GPL in 2008
  Extensively used in research
Now maintained by research community

## Slide 38: NOX Highlights
Linux
C++ and Python
Component system
Event-based programming model
Applications:
  Forwarding (reactive), topology discovery, host tracking, …

## Slide 39: NOX
Centralized programming model
High-level abstraction

## Slide 40: Programming Interface
Events
Namespace
Libraries
  Routing
  Packet classification
  DNS
  Network filtering

## Slide 41: POX
A new platform in pure Python
  Clean dependencies
  Take good things from NOX
  Target Linux, Mac OS, and Windows
Goal: Good for research
Non-goal: Performance