## Slide 1: An Overview of Software-Defined Network
Presenter: Xitao Wen

## Slide 2: Review: How a Router Works
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
* Excerpt from EECS 340 slides
Notes: Description
Problem: hardwired algorithms. no central view.

## Slide 3: Inside a Router
Routing Engine
Packet Forwarding Fabric
Input Ports
Output Ports
General-purpose CPU
ASIC, or specialized chips
Notes: Control plane
Data plane

## Slide 4: Separate Control-plane from Data-plane
Routing Engine
Packet Forwarding Fabric
Input Ports
Output Ports
Switch
Controller
Network Protocol over SSL

## Slide 7: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 8: OpenFlow Switch Model
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
SSL
hw
sw
OpenFlow Switch specification

## Slide 9: Flow Table Entry
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Matcher
Action
Counters
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Rewrite headers
Map to queue
+ mask
Packet + byte counters

## Slide 11: Secure Channel
SSL Connection, site-specific key
Controller discovery protocol
Encapsulate packets for controller
Send link/port state to controller

## Slide 12: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 13: OpenFlow Protocol
Connection
  Hello, Echo, Feature, Config…
Read-State
  Statistics, Port-status, Error
Modify-State
  Flow, Group, Config
Packet-in/Packet-out
Latest version: 1.5.0

## Slide 14: Reactive vs. Proactive (pre-populated)

## Slide 15: Reactive Flow-Push

## Slide 16: Proactive Flow-Push

## Slide 17: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 18: Key Task of OF Controller
OpenFlow protocol is largely deltas:
  Switch-to-Controller: changes of network state
  Controller-to-Switch: changes of configuration
It is a natural way to write control logic

## Slide 19: Architectural View: Network OS
OF Controller
Operating System
App
App
App
App
Switch
Switch
Switch

## Slide 20: Controller Platforms
Open Source
  OpenDaylight
  NOX/POX
  Floodlight
  Ryu
Proprietary
  BigSwitch
  HP
  NEC
  …

## Slide 22: Thank you!

## Slide 23: Back-up

## Slide 25: Experimenter’s Dream (Vendor’s Nightmare)
Standard
Network
Processing
hw
sw
Experimenter writes experimental code on switch/router
User-
defined
Processing

## Slide 29: OpenFlow Switch Model
Hardware
  One or more flow tables
  Group table (since Spec 1.1)
Software
  Secure Channel

## Slide 31: Furthermore, we want…
Isolation: Regular production traffic untouched
Virtualized and programmable: Different flows processed in different ways
Equipment we can trust in our wiring closet
Open development environment for all researchers (e.g. Linux, Verilog, etc).
Flexible definitions of a flow
  Individual application traffic
  Aggregated flows
  Alternatives to IP running side-by-side
  …

## Slide 32: Software-Defined Network

## Slide 33: Roadmap
Overview
Switch Model
OpenFlow Protocol
Controller
Switch
Controller
OpenFlow Protocol
Switch
Switch
Switch

## Slide 34: Step 1: Separate Control from Datapath

## Slide 35: Step 2: Cache flow decisions in datapath

## Slide 37: Evolving Protocol

## Slide 38: Current OpenFlow Hardware

## Slide 39: NOX: A Bit of History
NOX was the first SDN controller
Released under GPL in 2008
  Extensively used in research
Now maintained by research community

## Slide 40: NOX Highlights
Linux
C++ and Python
Component system
Event-based programming model
Applications:
  Forwarding (reactive), topology discovery, host tracking, …

## Slide 41: NOX
Centralized programming model
High-level abstraction

## Slide 42: Programming Interface
Events
Namespace
Libraries
  Routing
  Packet classification
  DNS
  Network filtering

## Slide 43: POX
A new platform in pure Python
  Clean dependencies
  Take good things from NOX
  Target Linux, Mac OS, and Windows
Goal: Good for research
Non-goal: Performance